## Slide 1: dfdl:lengthKind and dfdl:lengthUnits
Used frequently
  delimited
  implicit
    complex - length is sum of length of all children
    simple - length depends on type (for binary data)
  explicit - a constant or expression gives length
    needs dfdl:lengthUnits
Used in special cases
  prefixed
    needs dfdl:lengthUnits
  pattern - uses regular expressions (use as last resort only)
  endOfParent - not implemented (2025-12) by Daffodil
    See https://daffodil.apache.org/unsupported/

## Slide 2: Bit Order + Byte Order
Most Significant Bit First + Big Endian
Use Left-to-Right numbering to best visualize
Ex: Integer of 24 bits not byte aligned
Starts at bit 6 of byte 1
Byte:1 2 3 4
00000001 10111010 01001111 10100000
xxxxx 3 7 4 9 F 4
Bit 24
Bit 1

## Slide 3: Bit Order + Byte Order
Least Significant Bit First + Little Endian
Use Right-to-Left numbering to best visualize
Ex: Integer of 24 bits not byte aligned
Starts at bit 4 of byte 1
Byte: 4 3 2 1
00000001 10111010 01001111 10100000
xxxxx 3 7 4 9 F 4xxx
Bit 24
Bit 1

## Slide 4: More on Bit Order
Not about actual storage order
Rather: the way one chooses to number the bits
See: https://daffodil.apache.org/tutorials/bitorder.tutorial.tdml.xml

## Slide 5: TDML Data via Bits and Bytes
You can create binary data directly in TDML files
Often needed to construct detailed tests
  <document>
  <documentPart type="byte">01BA 4FA0</documentPart>
  <documentPart type="bits">
  00000001 10111010 01001111 10100000
  </documentPart>
  </document>
R-to-L order and LSBF are supported also